Previously On...
Voltage, Current and Resistance

---
Ohm’s Law

---
Previously On...
Voltage, Current and Resistance

---
Previously On...
Voltage, Current and Resistance
Inputs and Outputs

---
Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog

---
Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands

---
Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
pinMode(pin, INPUT/OUTPUT);
digitalWrite(pin, HIGH/LOW);
delay(ms);
analogWrite(pin, 0-255);

---
Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
pinMode(pin, INPUT/OUTPUT);
digitalWrite(pin, HIGH/LOW);
delay(ms);
analogWrite(pin, 0-255);
Functions

---
Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
pinMode(pin, INPUT/OUTPUT);
digitalWrite(pin, HIGH/LOW);
delay(ms);
analogWrite(pin, 0-255);
Functions
void setup() {}
void loop() {}

---
Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
pinMode(pin, INPUT/OUTPUT);
digitalWrite(pin, HIGH/LOW);
delay(ms);
analogWrite(pin, 0-255);
Functions
void setup() {}
void loop() {}
Comments
// Keep things clear

---
Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
pinMode(pin, INPUT/OUTPUT);
digitalWrite(pin, HIGH/LOW);
delay(ms);
analogWrite(pin, 0-255);
Functions
void setup() {}
void loop() {}
Comments
// Keep things clear
Variables
int led = 9;
int brightness = brightness + 1;

---
The Most Important Lesson
[Speaker Notes: This is why there’s a diversity problem in Engineering]

---
Inputs!
Input is any signal entering an electrical system
- Both digital and analog sensors are forms of input
- Input can also take many other forms: a keyboard, a mouse, infrared sensors, biometric sensors, touch sensors, cameras or just plain voltage from a circuit
- This is how you can make a computer react to the world around it

---
Digital Input
Like digital output, can only sense if a signal is high or low
- For Arduino
  - High is voltage above 3 V
  - Low is voltage below 1.5 V
- General category is “switches”
- Includes push buttons (momentary switches), toggle switches, knife switches (maintained switches), capacitive/touch switches, and many other sensors

---
Component Spotlight: The Push Button /
Momentary Switch

---
Push Button and Breadboard Connections
Our buttons have to bridge the gap on our breadboards
The top pins are connected to each other and so are the bottom ones

---
Using the Breadboard to Built a Simple Input Circuit
Remember our original circuit?

---
Using the Breadboard to Built a Simple Input Circuit
Remember our original circuit?
We’re going to wire that up again, but this time with a switch

---
Using the Breadboard to Built a Simple Input Circuit

---
Go ahead and plug your board in!

---
Adding Control

---
Adding Control
Any circuit that has meaningful input has some degree of control

---
Adding Control
Any circuit that has meaningful input has some degree of control
Microcontrollers allow us to assign different relationships between inputs and outputs

---
Project #3 – Lie Detector
Just give me 3 clock cycles with the perp...
Psuedo-code – how should this work?
if() statements / Boolean logic
Statement true?
NO
YES
Green LED turns on
Red LED turns on

---
Project #3 – Lie Detector
Inputs and Outputs
Inputs	Outputs
None	Green LED
	Red LED
Statement true?
NO
YES
Green LED turns on
Red LED turns on
[Speaker Notes: Our program is running hundreds of thousands of times every second]

---
Project #3 – Lie Detector
Schematic
You can leave the button on the breadboard- we’ll be using it again soon

---
Project #3 – Lie Detector
Wiring Diagram

---
Programming:  Conditional Statements
if()
Project #3 – Lie Detector
Conditional Statements
the if() statement

---
Project #3 – Lie Detector
Conditional Statements
If this is true

---
Project #3 – Lie Detector
Conditional Statements
If this is true
Do this

---
Project #3 – Lie Detector
Conditional Statements
If this is true
Do this
Otherwise

---
Project #3 – Lie Detector
Conditional Statements
If this is true
Do this
Otherwise
Do this

---
Boolean Operators
Boolean Operators
<Boolean>	True if:
(a)	a is true, HIGH or does not equal zero
(!a)	a is false, LOW or equals zero
(a) == (b)	a is equal to b
(a) != (b)	a is not equal to b
(a) > (b)	a is greater than b
(a) >= (b)	a is greater than or equal to b
(a) < (b)	a is less than b
(a) <= (b)	a is less than or equal to b
(a) && (b)	both a is true AND b is true
(a) || (b)	either a is true OR b is true

---
Déjà Vu

---
Project #3 – Lie Detector
Code Review
1	/*
2	* Test our if() statements
3	*/
4
5	// assign pin based off circuit
6	int red_led = 13;
7	int green_led = 12;
8
9	// these are the variables we'll play around with
10	int a = true;
11	int b = false;
12
13	// the setup function runs once when you press reset or power the board
14	void setup() {
15	pinMode(red_led, OUTPUT);
16	pinMode(green_led, OUTPUT);
17
18	// change the expression inside the if() and look at the results
19	if (a) {
20	digitalWrite(red_led, LOW);
21	digitalWrite(green_led, HIGH);
22	}
23	else {
24	digitalWrite(green_led, LOW);
25	digitalWrite(red_led, HIGH);
26	}
27	}
28
29	// the loop function runs over and over again forever
30	void loop() {
31
32	}

---
Project #3 – Lie Detector
Code Review
1	/*
2	* Test our if() statements
3	*/
4
5	// assign pin based off circuit
6	int red_led = 13;
7	int green_led = 12;
8
9	// these are the variables we'll play around with
10	int a = true;
11	int b = false;
12
13	// the setup function runs once when you press reset or power the board
14	void setup() {
15	pinMode(red_led, OUTPUT);
16	pinMode(green_led, OUTPUT);
17
18	// change the expression inside the if() and look at the results
19	if (b) {
20	digitalWrite(red_led, LOW);
21	digitalWrite(green_led, HIGH);
22	}
23	else {
24	digitalWrite(green_led, LOW);
25	digitalWrite(red_led, HIGH);
26	}
27	}
28
29	// the loop function runs over and over again forever
30	void loop() {
31
32	}

---
Project #3 – Lie Detector
Code Review
1	/*
2	* Test our if() statements
3	*/
4
5	// assign pin based off circuit
6	int red_led = 13;
7	int green_led = 12;
8
9	// these are the variables we'll play around with
10	int a = true;
11	int b = false;
12
13	// the setup function runs once when you press reset or power the board
14	void setup() {
15	pinMode(red_led, OUTPUT);
16	pinMode(green_led, OUTPUT);
17
18	// change the expression inside the if() and look at the results
19	if (!b) {
20	digitalWrite(red_led, LOW);
21	digitalWrite(green_led, HIGH);
22	}
23	else {
24	digitalWrite(green_led, LOW);
25	digitalWrite(red_led, HIGH);
26	}
27	}
28
29	// the loop function runs over and over again forever
30	void loop() {
31
32	}

---
Project #3 – Lie Detector
Code Review
1	/*
2	* Test our if() statements
3	*/
4
5	// assign pin based off circuit
6	int red_led = 13;
7	int green_led = 12;
8
9	// these are the variables we'll play around with
10	int a = true;
11	int b = false;
12
13	// the setup function runs once when you press reset or power the board
14	void setup() {
15	pinMode(red_led, OUTPUT);
16	pinMode(green_led, OUTPUT);
17
18	// change the expression inside the if() and look at the results
19	if (!a) {
20	digitalWrite(red_led, LOW);
21	digitalWrite(green_led, HIGH);
22	}
23	else {
24	digitalWrite(green_led, LOW);
25	digitalWrite(red_led, HIGH);
26	}
27	}
28
29	// the loop function runs over and over again forever
30	void loop() {
31
32	}

---
Project #3 – Lie Detector
Code Review
1	/*
2	* Test our if() statements
3	*/
4
5	// assign pin based off circuit
6	int red_led = 13;
7	int green_led = 12;
8
9	// these are the variables we'll play around with
10	int a = 9;
11	int b = 5;
12
13	// the setup function runs once when you press reset or power the board
14	void setup() {
15	pinMode(red_led, OUTPUT);
16	pinMode(green_led, OUTPUT);
17
18	// change the expression inside the if() and look at the results
19	if (a > b) {
20	digitalWrite(red_led, LOW);
21	digitalWrite(green_led, HIGH);
22	}
23	else {
24	digitalWrite(green_led, LOW);
25	digitalWrite(red_led, HIGH);
26	}
27	}
28
29	// the loop function runs over and over again forever
30	void loop() {
31
32	}

---
Project #3 – Lie Detector
Code Review
1	/*
2	* Test our if() statements
3	*/
4
5	// assign pin based off circuit
6	int red_led = 13;
7	int green_led = 12;
8
9	// these are the variables we'll play around with
10	int a = 9;
11	int b = 5;
12
13	// the setup function runs once when you press reset or power the board
14	void setup() {
15	pinMode(red_led, OUTPUT);
16	pinMode(green_led, OUTPUT);
17
18	// change the expression inside the if() and look at the results
19	if (a < b) {
20	digitalWrite(red_led, LOW);
21	digitalWrite(green_led, HIGH);
22	}
23	else {
24	digitalWrite(green_led, LOW);
25	digitalWrite(red_led, HIGH);
26	}
27	}
28
29	// the loop function runs over and over again forever
30	void loop() {
31
32	}

---
Project #3 – Lie Detector
Code Review
1	/*
2	* Test our if() statements
3	*/
4
5	// assign pin based off circuit
6	int red_led = 13;
7	int green_led = 12;
8
9	// these are the variables we'll play around with
10	int a = true;
11	int b = 5;
12
13	// the setup function runs once when you press reset or power the board
14	void setup() {
15	pinMode(red_led, OUTPUT);
16	pinMode(green_led, OUTPUT);
17
18	// change the expression inside the if() and look at the results
19	if (b > 5 || a) {
20	digitalWrite(red_led, LOW);
21	digitalWrite(green_led, HIGH);
22	}
23	else {
24	digitalWrite(green_led, LOW);
25	digitalWrite(red_led, HIGH);
26	}
27	}
28
29	// the loop function runs over and over again forever
30	void loop() {
31
32	}

---
Project #3 – Lie Detector
Code Review
1	/*
2	* Test our if() statements
3	*/
4
5	// assign pin based off circuit
6	int red_led = 13;
7	int green_led = 12;
8
9	// these are the variables we'll play around with
10	int a = true;
11	int b = 5;
12
13	// the setup function runs once when you press reset or power the board
14	void setup() {
15	pinMode(red_led, OUTPUT);
16	pinMode(green_led, OUTPUT);
17
18	// change the expression inside the if() and look at the results
19	if (b > 5 && a) {
20	digitalWrite(red_led, LOW);
21	digitalWrite(green_led, HIGH);
22	}
23	else {
24	digitalWrite(green_led, LOW);
25	digitalWrite(red_led, HIGH);
26	}
27	}
28
29	// the loop function runs over and over again forever
30	void loop() {
31
32	}

---
Project #3 – Lie Detector
Code Review
1	/*
2	* Test our if() statements
3	*/
4
5	// assign pin based off circuit
6	int red_led = 13;
7	int green_led = 12;
8
9	// these are the variables we'll play around with
10	int a = true;
11	int b = 5;
12
13	// the setup function runs once when you press reset or power the board
14	void setup() {
15	pinMode(red_led, OUTPUT);
16	pinMode(green_led, OUTPUT);
17
18	// change the expression inside the if() and look at the results
19	if (b >= 5 && a) {
20	digitalWrite(red_led, LOW);
21	digitalWrite(green_led, HIGH);
22	}
23	else {
24	digitalWrite(green_led, LOW);
25	digitalWrite(red_led, HIGH);
26	}
27	}
28
29	// the loop function runs over and over again forever
30	void loop() {
31
32	}

---
Boolean Operators
<Boolean>	True if:
(a)	a is true, HIGH or does not equal zero
(!a)	a is false, LOW or equals zero
(a) == (b)	a is equal to b
(a) != (b)	a is not equal to b
(a) > (b)	a is greater than b
(a) >= (b)	a is greater than or equal to b
(a) < (b)	a is less than b
(a) <= (b)	a is less than or equal to b
(a) && (b)	both a is true AND b is true
(a) || (b)	either a is true OR b is true

---
Project #4 – Button/Maintained Switch Switch
Who you callin’ momentary?
Psuedo-code – how should this work?
LED turns off
Rinse & Repeat
Button Pressed?
LED
status?
YES
LED turns on
digitalRead()
OFF
ON

---
Project #4 – Button/Maintained Switch Switch
Who you callin’ momentary?
Psuedo-code – how should this work?
LED turns off
Rinse & Repeat
Button Pressed?
LED
status?
Pressed Before?
YES
NO
LED turns on
digitalRead()
OFF
ON

---
Project #4 – Button/Maintained Switch Switch
Inputs and Outputs
LED turns off
Rinse & Repeat
Button Pressed?
LED
status?
Pressed Before?
YES
NO
LED turns on
Inputs	Outputs
Push Button	LED
OFF
ON
[Speaker Notes: Our program is running hundreds of thousands of times every second]

---
Transitioning to Micro-control
Output & Input

---
Transitioning to Micro-control
Output & Input

---
Project #4 – Button/Maintained Switch Switch
Wiring Diagram

---
Project #4 – Button/Maintained Switch Switch
Wiring Diagram
WRONG!!!

---
This Part Is Good

---
So This Must Be Bad…

---
So This Must Be Bad…
But Why?!

---
Another Water Analogy

---
Analogy Continued...

---
Analogy Continued...
?

---
All Stopped Up

---
All Stopped Up
(kinda)

---
Switch Off

---
Switch On

---
Switch Off?!

---
Analogy Extended
(Thin but holding)

---
So This Approach...

---
Doesn’t Work!

---
What About...

---
Changing Bathroom Fixtures?

---
Getting Rid of the Unnecessary Crap

---
Changing the Viewpoint

---
Changing the Viewpoint

---
Changing the Viewpoint

---
Changing the Viewpoint

---
Switch Off

---
Switch On

---
Switch Right After Off

---
Switch Off

---
Stop Playin’ With the Commode!!

---
Possible Solution

---
How Do We Get Here?
?

---
Resistance Analogy
V
Big Pipe == Lower Resistance
Small Pipe == Higher Resistance
Water
Tower
Water
Tower

---
How Do We Get Here?
?

---
The Pull-Up Resistor!

---
But There’s A Trade-Off Between This...

---
…And This

---
It’s All About Compromise
10kΩ is a good value
(brown-black-black-red-gold)
or
(brown-black-orange-gold)

---
Decoding Resistor Values

---
Project #4 – Button/Maintained Switch Switch
Input Schematic
Schematic of Pull-Up Resistor and Switch

---
Project #4 – Button/Maintained Switch Switch
Full Schematic
And the output is still the same as Project 1!

---
Project #4 – Button/Maintained Switch Switch
Wiring Diagram

---
Project #4 – Button/Maintained Switch Switch
Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
[Speaker Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.]

---
Project #4 – Button/Maintained Switch Switch
Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
[Speaker Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.]

---
Project #4 – Button/Maintained Switch Switch
Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
[Speaker Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.]

---
Project #4 – Button/Maintained Switch Switch
Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
  ex: digitalRead(2);
[Speaker Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.]

---
Project #4 – Button/Maintained Switch Switch
Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
  ex: digitalRead(2);
  ex: int button_state = digitalRead(2);
[Speaker Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.]

---
Project #4 – Button/Maintained Switch Switch
Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
  ex: digitalRead(2);
  ex: int button_state = digitalRead(2);
button_state will either be HIGH or LOW
HIGH if switch is off, LOW if switch is on
[Speaker Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.]

---
Project #4 – Button/Maintained Switch Switch
Code Review

---
Code Review Continued

---
Code Review Continued

---
Project #4 – Button/Maintained Switch Switch
Puzzles
Challenge 4a – Wire another LED. Make the button turn one off and the other on
Challenge 4b – Make an LED blink when you press the button (hint: look at File>Examples>Digital>Blink Without Delay)
Challenge 4c – Make an LED alternate between off, on and blink by pressing the button

---
Special Thanks:
www.sparkfun.com
6175 Longbow Drive, Suite 200
Boulder, Colorado 80301