Previously On...
Digital Inputs

---
Previously On...
Digital Inputs
if() statements

---
Boolean Operators
Boolean Operators
<Boolean>	True if:
(a)	a is true, HIGH or does not equal zero
(!a)	a is false, LOW or equals zero
(a) == (b)	a is equal to b
(a) != (b)	a is not equal to b
(a) > (b)	a is greater than b
(a) >= (b)	a is greater than or equal to b
(a) < (b)	a is less than b
(a) <= (b)	a is less than or equal to b
(a) && (b)	both a is true AND b is true
(a) || (b)	either a is true OR b is true

---
Previously On...
Digital Inputs
if() statements

---
Previously On...
Digital Inputs
if() statements
Pull-up resistors

---
Seriously, the one thing to take away
[Speaker Notes: This is why there’s a diversity problem in Engineering]

---
Project #5 – Night Light
How Dark Is Too Dark?
Psuedo-code – how should this work?
LED turns on
Rinse & Repeat
Check How Dark It Is
How Dark Is It?
LED turns off
IT’S FINE
TOO DARK!
analogRead()

---
Project #4 - Night Light
Inputs and Outputs
LED turns on
Rinse & Repeat
Check How Dark It Is
How Dark Is It?
LED turns off
Inputs	Outputs
Photoresistor	LED
IT’S FINE
TOO DARK!

---
The Voltage Divider

---
The Voltage Divider

---
The Voltage Divider
“From each according to their ability, to each according to their need.”

---
The Voltage Divider
How many carrots does the fairy have left at this point?

---
The Voltage Divider
How many carrots does the fairy have left at this point?

---
The Voltage Divider
How many carrots does the fairy have left at this point?

---
The Voltage Divider
How many carrots does the fairy have left at this point?

---
The Voltage Divider
How many carrots does the fairy have left at this point?

---
The Switch-Over

---
Project #4 – Night Light
Schematic

---
Project #4 – Night Light
Wiring Diagram

---
Project #4 – Night Light
int sensor_val = analogRead(pin);
pin – refers to the analog input pin (limited to pins A0, A1, A2, A3, A4 and A5)
Arduino uses a 10-bit analog-to-digital converter (ADC):
This means that sensor_val is always a number between 0 and 1023
  - Minimum Carrots → 0
  - Maximum Carrots → 1023

---
Determining Analog Values
But the top bunny is always going to get some carrots, so we can’t really get to 1023
And we can’t really make our bottom bunny so small that it gets 0 carrots
So how do we determine the minimum and maximum numbers for our circuit?
Do math

---
Determining Analog Values
But the top bunny is always going to get some carrots, so we can’t really get to 1023
And we can’t really make our bottom bunny so small that it gets 0 carrots
So how do we determine the minimum and maximum numbers for our circuit?
- Do math
- Ask the microcontroller

---
Using Serial Communication
Using Serial Communication
Method used to transfer data between two devices.
Data passes between the computer and Arduino through the Universal Serial Bus (USB!) cable. Data is transmitted as zeros (‘0’) and ones (‘1’) sequentially.
Arduino dedicates Digital I/O pin # 0 to receiving and Digital I/O pin #1 to transmit.
[Speaker Notes: Serial is the same for novels, soldiers, murders, killers, communication For this reason, we typically do not use Digital I/O 0 or 1 for anything in our designs.]

---
Displaying the Serial Monitor

---
A Tour of the Serial Monitor

---
A Tour of the Serial Monitor

---
A Tour of the Serial Monitor

---
A Tour of the Serial Monitor

---
A Tour of the Serial Monitor

---
A Tour of the Serial Monitor

---
Baud Rate
How do we know how many 0’s and 1’s there are?
We tell how the computer and microcontroller how long a signal has to be high or low to count as a 1 or a 0 by setting the baud rate
For our purposes it doesn’t really matter what the baud rate is, it’s just important that the microcontroller and computer agree!

---
Serial Commands
Serial.begin(baud_rate);
ex: Serial.begin(9600);
Serial.print(“Text”);
Serial.print(variable);
Serial.println(“Text”);
Serial.println(variable);

---
Ask Arduino - Code Review

---
Serial Communication:
Serial Debugging
Serial Communication:
Serial Debugging
void loop()
{
int xVar = 10;
Serial.print ( “Variable xVar is “ ) ;
Serial.println ( xVar ) ;
}

---
Serial Communication:
Serial Troubleshooting
Serial Communication:
Serial Troubleshooting
void loop ( )
{
  Serial.print (“Digital pin 9: “);
  Serial.println (digitalRead(9));
}

---
Night Light - Code Review

---
Analog Sensors
Analog Sensors
Examples:
Sensors	Variables
Photoresistor	light_level
Microphone	sound_volume
Temp Sensor	temp
Flex Sensor	bend
Accelerometer	tilt, acceleration

---
Trimpot (Potentiometer)
Variable Resistor
Trimpot (Potentiometer)
Variable Resistor
fixed
end
wiper
fixed
end

---
Trimpot (Potentiometer)
Variable Resistor

---
Trimpot (Potentiometer)
What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
This makes potentiometers excellent controllers for physical computing “settings”
Can we think of any examples?

---
Trimpot (Potentiometer)
What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
This makes potentiometers excellent controllers for physical computing “settings”
Can we think of any examples?
But what if the setting we want to control has less (or more) than 1023 values? Or if we want it not to start at 0?

---
Trimpot (Potentiometer)
What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
This makes potentiometers excellent controllers for physical computing “settings”
Can we think of any examples?
But what if the setting we want to control has less (or more) than 1023 values? Or if we want it not to start at 0?
Do math

---
Trimpot (Potentiometer)
What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
This makes potentiometers excellent controllers for physical computing “settings”
Can we think of any examples?
But what if the setting we want to control has less (or more) than 1023 values? Or if we want it not to start at 0?
Do math
Get the microcontroller to do it for us

---
Map Command
int new_var = map(old_var, old_low, old_high, new_low, new_high);
    ex: offset_val = map(val, 0, 100, -50, 50);
    ex: reverse_val = map(val, 1, 100, 100, 1);
    ex: write_val = map(read_val, 0, 1023, 0, 255);

---
Project #5 – Real Time Color Mixer
Tying it all together...
Psuedo-code – how should this work?
Change to green
Light green LED
Button A Pressed?
Pressed Before?
Current LED?
Change to blue
Light yellow LED
GREEN
YES
NO
Change to red
Light red LED
Write a scaled trimpot value to red pin of RGB LED
Button B Pressed?
Read trimpot
Current LED?
Write a scaled trimpot value to green pin of RGB LED
GREEN
YES
Write a scaled trimpot value to blue pin of RGB LED
BLUE
RED
BLUE
RED

---
Project #5 – Inputs and Outputs
Inputs	Outputs
a “Select” Button	Red Indicator
an “Adjust” Button	Green Indicator
Trimpot	Blue Indicator
	RGB LED

---
Project #5 – Real Time Color Mixer
Schematic

---
Project #5 – Real Time Color Mixer
Wiring Diagram

---
Where To Go From Here:

---
Special Thanks:
www.sparkfun.com
6175 Longbow Drive, Suite 200
Boulder, Colorado 80301