## Slide 1: Previously On...
Digital Inputs

## Slide 2: Previously On...
Digital Inputs
if() statements

## Slide 3: Boolean Operators
<Boolean> | True if:
(a) | a is true, HIGH or does not equal zero
(!a) | a is false, LOW or equals zero
(a) == (b) | a is equal to b
(a) != (b) | a is not equal to b
(a) > (b) | a is greater than b
(a) >= (b) | a is greater than or equal to b
(a) < (b) | a is less than b
(a) <= (b) | a is less than or equal to b
(a) && (b) | both a is true AND b is true
(a) ¦¦ (b) | either a is true OR b is true

## Slide 4: Previously On...
Digital Inputs
if() statements

## Slide 5: Previously On...
Digital Inputs
if() statements
Pull-up resistors

## Slide 6: Seriously, the one thing to take away
Notes: This is why there’s a diversity problem in Engineering

## Slide 7
Project #5 – Night Light
How Dark Is Too Dark?
Psuedo-code – how should this work?
Check How Dark It Is
How Dark Is It?
IT’S FINE
TOO DARK!
LED turns on
Rinse & Repeat
LED turns off
analogRead()

## Slide 8: Project #4 - Night Light Inputs and Outputs
Check How Dark It Is
How Dark Is It?
IT’S FINE
TOO DARK!
LED turns on
Rinse & Repeat
LED turns off
Inputs | Outputs
Photoresistor | LED

## Slide 9: The Voltage Divider

## Slide 10: The Voltage Divider

## Slide 11: The Voltage Divider
“From each according to their ability, to each according to their need.”

## Slide 12: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 13: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 14: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 15: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 16: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 17: The Switch-Over

## Slide 18: Project #4 – Night Light Schematic

## Slide 19: Project #4 – Night Light Wiring Diagram

## Slide 20: Project #4 – Night Light
int sensor_val = analogRead(pin);
pin – refers to the analog input pin (limited to pins A0, A1, A2, A3, A4 and A5)
Arduino uses a 10-bit analog-to-digital converter (ADC):
This means that sensor_val is always a number between 0 and 1023
  Minimum Carrots → 0
  Maximum Carrots → 1023

## Slide 21: Determining Analog Values
But the top bunny is always going to get some carrots, so we can’t really get to 1023
And we can’t really make our bottom bunny so small that it gets 0 carrots
So how do we determine the minimum and maximum numbers for our circuit?
Do math

## Slide 22: Determining Analog Values
But the top bunny is always going to get some carrots, so we can’t really get to 1023
And we can’t really make our bottom bunny so small that it gets 0 carrots
So how do we determine the minimum and maximum numbers for our circuit?
Do math
Ask the microcontroller

## Slide 23: Using Serial Communication
Method used to transfer data between two devices.
Arduino dedicates Digital I/O pin # 0 to receiving and Digital I/O pin #1 to transmit.
Data passes between the computer and Arduino through the Universal Serial Bus (USB!) cable. Data is transmitted as zeros (‘0’) and ones (‘1’) sequentially.
Notes: Serial is the same for novels, soldiers, murders, killers, communication
For this reason, we typically do not use Digital I/O 0 or 1 for anything in our designs.

## Slide 24: Displaying the Serial Monitor

## Slide 25: A Tour of the Serial Monitor

## Slide 26: A Tour of the Serial Monitor

## Slide 27: A Tour of the Serial Monitor

## Slide 28: A Tour of the Serial Monitor

## Slide 29: A Tour of the Serial Monitor

## Slide 30: A Tour of the Serial Monitor

## Slide 31: Baud Rate
How do we know how many 0’s and 1’s there are?
We tell how the computer and microcontroller how long a signal has to be high or low to count as a 1 or a 0 by setting the baud rate
For our purposes it doesn’t really matter what the baud rate is, it’s just important that the microcontroller and computer agree!

## Slide 32: Serial Commands
Serial.begin(baud_rate);
ex: Serial.begin(9600);
Serial.print(“Text”);
Serial.print(variable);
Serial.println(“Text”);
Serial.println(variable);

## Slide 33: Ask Arduino - Code Review

## Slide 34: Serial Communication: Serial Debugging
void loop()
{
int xVar = 10;
Serial.print ( “Variable xVar is “ ) ;
Serial.println ( xVar ) ;
}

## Slide 35: Serial Communication: Serial Troubleshooting
void loop ( )
{
Serial.print (“Digital pin 9: “);
Serial.println (digitalRead(9));
}

## Slide 36: Night Light - Code Review

## Slide 37: Analog Sensors
Examples:
Sensors | Variables
Photoresistor | light_level
Microphone | sound_volume
Temp Sensor | temp
Flex Sensor | bend
Accelerometer | tilt, acceleration

## Slide 38: Trimpot (Potentiometer) Variable Resistor
wiper
fixed
end
fixed
end

## Slide 39: Trimpot (Potentiometer) Variable Resistor

## Slide 40: Trimpot (Potentiometer) What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
  This makes potentiometers excellent controllers for physical computing “settings”
  Can we think of any examples?

## Slide 41: Trimpot (Potentiometer) What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
  This makes potentiometers excellent controllers for physical computing “settings”
  Can we think of any examples?
  But what if the setting we want to control has less (or more) than 1023 values? Or if we want it not to start at 0?

## Slide 42: Trimpot (Potentiometer) What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
  This makes potentiometers excellent controllers for physical computing “settings”
  Can we think of any examples?
  But what if the setting we want to control has less (or more) than 1023 values? Or if we want it not to start at 0?
    Do math

## Slide 43: Trimpot (Potentiometer) What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
  This makes potentiometers excellent controllers for physical computing “settings”
  Can we think of any examples?
  But what if the setting we want to control has less (or more) than 1023 values? Or if we want it not to start at 0?
    Do math
    Get the microcontroller to do it for us

## Slide 44: Map Command
int new_var = map(old_var, old_low, old_high, new_low, new_high);
ex: offset_val = map(val, 0, 100, -50, 50);
ex: reverse_val = map(val, 1, 100, 100, 1);
ex: write_val = map(read_val, 0, 1023, 0, 255);

## Slide 45
Project #5 – Real Time Color Mixer
Tying it all together...
Psuedo-code – how should this work?
Button A Pressed?
YES
Current LED?
BLUE
RED
Change to green
Change to red
Pressed Before?
NO
Change to blue
GREEN
Light green LED
Light yellow LED
Light red LED
Button B Pressed?
YES
Current LED?
BLUE
RED
Write a scaled trimpot value to red pin of RGB LED
Write a scaled trimpot value to blue pin of RGB LED
Read trimpot
Write a scaled trimpot value to green pin of RGB LED
GREEN

## Slide 46
Project #5 – Inputs and Outputs
Inputs | Outputs
a “Select” Button | Red Indicator
an “Adjust” Button | Green Indicator
Trimpot | Blue Indicator
 | RGB LED

## Slide 47: Project #5 – Real Time Color Mixer Schematic

## Slide 48: Project #5 – Real Time Color Mixer Wiring Diagram

## Slide 49: Where To Go From Here:

## Slide 50: Special Thanks:
www.sparkfun.com
6175 Longbow Drive, Suite 200
Boulder, Colorado 80301